## Slide 1: Continuous Wave Spectroscopy

## Slide 2: Resonator Spectroscopy
Wideband scan from 2-9GHz on VNA
  Ensure readout chain is performing to spec
  min
Zoom on resonators (6-7GHz)
  Find peaks for readout resonators,
  1 min
Zoom on resonators (individual) vs power
  Ensure `punchout´ response to know if qubits survived fab
  shift for extracting later
  , vs. Power,
  min per resonator

## Slide 3: Qubit Spectroscopy (Rough)
CW qubit spectroscopy
  Sweep qubit frequency to get rough response
  min per qubit
  rough
CW Spec vs Power
  Zoom in range of design,
  find ,
  min per qubit

## Slide 4: Pulsed Spectroscopy

## Slide 5: Resonator Spectroscopy (Pulsed)
Use previous information to guide initial frequency guesses
  Can now perform multiplexed readout of the signals and read all resonators at once

## Slide 6: Single Qubit Control (Rough)
Find pulse roughly (Rabi, parallel)
  Sweep amplitude for fixed
  Obtain pulse amplitudes
  min
Refine to true values (parallel)
  Measure Ramsey detuned by MHz from rough
  min
At this point can measure T1, T2, T2*
  Typically move onto readout optimization/discrimination
  IQ balancing (optimizing pulse upconversion)

## Slide 7: Mixer Calibration
Once operating frequency is found we can balance the -Wave mixers for the qubit signal
Supress LO leakage by adjusting DC offsets between IQ ports
Supress image sideband by adjusting relative gain and phase between IQ ports

## Slide 8: Readout Optimization (Round 1)
Pulsed resonator spectroscopy as a function of qubit state
  Find maximum SNR in IQ plane
Convert to Single Shot measurement and generate discriminator
  Nearest centroid, SVM, etc…
Optimize readout pulse-length and RO pulse amplitude to maximize
  Can hold-off if interested in state

## Slide 9: State Calibration
Calibrate for a , -pulse
  Use rough anharmonicity from previous measurement, sweep amp
Calibrate, Ramsey for exact anharmonicity,

## Slide 10: Readout Optimization (Round 2)
Resonator spectroscopy vs. Readout State
  Maximize SNR using triangular area (Heron’s formula)
Proper Optimization of readout pulse, integration time, matched filters, IQ mixers, etc...
Characterize Confusion Matrix on 0,1 subspace and 0,1,2

## Slide 11: DRAG Optimization
Phase & Leakage,
  Error Amplification on dynamical detuning vs
Rabi Refined
  Error amplification on |A|
Leakage RB
  RB vs. optimal pair
  Minimize leakage rate of state

## Slide 12: Verification of Performance (RB)
Want to quantify the errors associated with our tuned up gates
Apply a protocol called Randomized Benchmarking (RB)
Finds us the average error per 1-Qubit operation
Randomly select a sequence of gates of depth, m
Find the gate which inverts the m-depth sequence
Repeat this k times and average the results
Fit the average decay and extract the error per gate

## Slide 13
Readout
Single Qubit
Manually Disconnect VNA
Parallelized
Not Parallelized
Connect to Spectrum Analyzer IQ Balancing
Connect to Spectrum Analyzer
Calibration Flow Outline
Resonator Wide
Resonator Zoom
Qubit Punchout
CW Qubit Spectroscopy
Pulsed Readout Spectroscopy
Rabi Driving
Ramsey Driving
Readout Optimization g-e
Single Shot/ State Discrimination
state spectroscopy
state Rabi
Readout Optimization g-e-f
DRAG Calibration
Refined Driving Amplitude
Single Qubit RB